## Slide 1: RS485 serial bus communication with.NET Core, Raspberry PI and Arduino
Marco Parenzan

## Slide 2: Preparing Raspberry Pi for the first time
Download last raspbian image from https://www.raspberrypi.org/downloads/raspbian/
  Extract the img file from the zip
Write image to the SD card with Etcher
  download etcher from https://etcher.io/

## Slide 3: Configuring SD card to connect to the RPI
From the Windows Explorer you see a couple of drives:
  Boot, the boot partition, accessible from windows
  Usb Drive, the linux partition
Identify the cmdline.txt file
Choose a private class to connected your PC with RPI via Ethernet cable (ex. 192.168.100.100)
  ip=192.168.100.100::192.168.1.1:255.255.255.0:rpi:eth0:off
Configure this on cmdline.txt

## Slide 4: Configure your Ethernet to connect to the RPI for the first time (make equivalent chooses on Linux or Mac)
...and then download and install PuTTY (https://www.putty.org/) to connect

## Slide 5: Entering Raspberry PI from the console for the first time
Connect as pi|raspberry (standard user and password) for the first time

## Slide 6: Configuring WiFi on the Raspberry
https://www.raspberrypi.org/documentation/configuration/wireless/wireless-cli.md
Have a WiFi with WPA/WPA2 with SSID and a PSK
Open wifi configuration file
  sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
Configure your wifi
Then reboot
And then you can identify your wifi ip address from the router or with the following command
  sudo ifconfig

## Slide 7: Installing .NET Core on Raspberry PI
Best way (thanks to Scott Hanselman tip)
  https://www.hanselman.com/blog/BuildingRunningAndTestingNETCoreAndASPNETCore21InDockerOnARaspberryPiARM32.aspx
  Look at the current Docker file (docker is more useful to deploy and run .NET Core more than dev)
  https://github.com/dotnet/dotnet-docker/blob/master/2.1/sdk/stretch/arm32v7/Dockerfile
In general
  Install all the updates
  Download package (check if the last version – there is a variable for this)
  Create directory
  Unpack
  Set global variables
  Lauch with dotnet command!

## Slide 8: Best practices writing code on Raspberry PI
Write code on your laptop
Test and debug on your laptop as much as you can
Commit code onto a GitHub repository
Then on the raspberry
  Clone the repository
  Edit source files with nano <filename>
  dotnet build (from the root of the project) builds the project
  Output is container in bin/Debug/netstandard2.1 folder
  dotnet run lauch from the project folder
  dotnet <dllname> from the output folder

## Slide 9: Get the code
git clone https://github.com/marcoparenzan/RS485Communication.git
nano RS485Communication.cs

## Slide 10: SerialPort.Core does not work on Linux 
Common issue
  https://github.com/dotnet/core/issues/740
Use an open source reimplementation
  Install-Package SerialPortStream -Version 2.1.4
  https://github.com/jcurl/SerialPortStream

## Slide 11: SerialPortStream does not work on Rpi 
Dependency on libnserial.so* libs
Solution
  Recompile natively on RPI (https://www.raspberrypi.org/forums/viewtopic.php?t=62344)
    sudo apt-get update && sudo apt-get upgrade sudo apt-get install cmake
  Clone GIT source from https://github.com/jcurl/SerialPortStream
  cd seriallinux
  ./build.sh
Set environmental variables
  https://github.com/jcurl/SerialPortStream/blob/v2.x/README.md
  export LD_LIBRARY_PATH=`pwd`/bin/usr/local/lib:$LD_LIBRARY_PATH
Cp all libnserial.so* into netstandard2.1 dir